## Slide 1: ECEN 214, Spring 2022 Electrical Circuit Theory
Prof. Adam Birchfield
Dept. of Electrical and Computer Engineering
Texas A&M University
abirchfield@tamu.edu
Class 17: Impedance

## Slide 2: Assignments
Zybook Chapter 7
Quiz next class on AC circuits and impedance
Start working on HW 7A
Sign up for the power plant tour by this Friday. The tour is next Tuesday at 3pm (April 5th)
Review in-class examples and notes
  Practice, practice, practice!
Don’t forget, you need to go to office hours at least once in either March or April. Bring at least one technical question!
Source: https://www.btutilities.com/about-btu/btu-history/

## Slide 3: Review: Phasor Analysis
A phasor is a complex number that represents a cosine-valued AC function
The Root Mean Square (RMS) for cosine is found by dividing the maximum value by
In polar form,, a phasor represents the RMS voltage or current and phase angle
Conversions to rectangular form: a+jb, and back can be done with these identities:
Complex number addition can be done in rectangular form, and complex number multiplication can be done in polar form.
Phasor diagrams have the real part on the x axis and imaginary part on the y axis.
The angular frequency is .
KVL, KCL, and Ohm’s law all apply with AC phasor analysis exactly as with DC.
This means you can use Node-Voltage and Mesh-Current analysis methods too.

## Slide 4: Why Does Phasor Analysis Work?
We can represent a sinusoidal voltage or current with a complex number, and all the circuit laws will apply to that complex number.
It’s much easier that constantly having to apply trigonometric identities
Euler’s identity says
So we can see that
Try adding and subtracting cosines (with sum and difference identities) and see that you get the same result as adding and subtracting the complex numbers
Try multiplying and dividing the cosines (with product and quotient identities) and see that you get the same results as adding and subtracting the complex numbers.
RMS is used instead of peak because of power considerations, which we will discuss next week.

## Slide 5: Resistors and AC Phasors
Resistors still have Ohm’s law, which applies with phasors
Frequency is not involved
+
_

## Slide 6: Inductors and AC
Remember the equation for inductors?
If v(t) and i(t) are cosine functions
So for phasor analysis we need to multiply by and have a +90 degree phase shift (cos to sin)
No differential equations! Just multiply by
For this example
What if frequency was really high? Really low?
+
_
60 Hz is the frequency

## Slide 7: Impedance
You can do a similar analysis and find the following equation for capacitors
Both inductors and capacitors are algebraic rather than differential in AC
We use the concept of “impedance” which is like a complex resistance, to represent resistors, inductors, and capacitors
Z is a complex number, the impedance, that depends on the inductors, resistors, and capacitors
Element | Time Domain | Phasor Domain | Z (impedance)
Resistor |  |  | 
Inductor |  |  | 
Capacitor |  |  | 
Element | Time Domain | Phasor Domain | Z (impedance)
Resistor |  |  | 
Inductor |  |  | 
Capacitor |  |  | 
How do inductors and capacitors behave differently in high and low frequencies?
Remember, DC steady-state is sort of like
Units of impedance are Ohms for all three!

## Slide 8: Example 1
Find the current phasor I for this 1 kHz circuit
Impedance of the resistor?
Impedance of the capacitor?
You can treat impedances just like complex resistances! The capacitor and resistor are in parallel
80
+
_
What would this be as a time function?
What would it be in a lower frequency?

## Slide 9: Example 2
Solve for the phasor for this circuit if it is operated at 400 Hz
40
+
_
+
_

## Slide 10: Example 3
Solve for current . The impedance is already given, so you don’t need the frequency
80
100
+
_

## Slide 11: Example 4
Find the time signal (Try using mesh-current analysis and node-voltage analysis.)
10W
2W
+
_
+
_
4 mH
300