## Slide 1: ECEN 616, Fall 2022 Methods of Electric Power System Analysis
Prof. Adam Birchfield
Dept. of Electrical and Computer Engineering
Texas A&M University
abirchfield@tamu.edu
Class 3: Principles of Electromagnetic Transient Analysis, Part 3

## Slide 2: Announcements
Course website: https://birchfield.engr.tamu.edu/616f22/
Syllabus on website gives detailed course info
Textbooks: Greenwood and Dommel
Make sure you can get access to EMTP in the basement lab of Wisenbaker 061, or through the TAMU Engineering VDI
For Wednesday (8/31), try to do Example 1 using EMTP
Friday is practice oral exam (signing up today)

## Slide 3: What This Class Will Cover
Electromagnetic Transients Theory
  Principles of transient analysis
  Analytical methods for solving transient problems
  Numerical methods for solving transient problems
  Block element models
  Transmission line models (overhead/underground, single-phase/multi-phase, frequency dependent)
  Transformer models
Electromagnetic Transients Applications
  Capacitor and reactor switching
  Transmission line switching
  Lightning studies and insulation coordination
  Transients with power-electronics components
  Electric field coupling

## Slide 4: Principles of Electromagnetic Transient Analysis
You must understand your model.
Models must be validated.
  Against your intuition (try ultra-simple, very predictable cases)
  Against other models (both simpler and more complex)
  Against real data (field measurement and lab tests)
EMT studies apply best to certain studies.
  Transient conditions as opposed to steady-state
  Very high frequency, short-duration events (roughly 1 kHz to 1 GHz)
  Transmission or distribution, balanced or unbalanced
  Electronic controls, lightning, and switching surges are key applications
Circuit theory fundamentals always apply.
  KVL, KCL, equations for RLC
  Conservation of charge, conservation of energy

## Slide 5: Principles of Electromagnetic Transient Analysis
Power flow assumptions do NOT always apply.
  Voltage and current are not phasors, be careful with reactive power
  Impedance varies with frequency, t-lines aren’t usually PI models
  Three-phase systems will usually be modeled in full, not with positive sequence
  System is not in steady state, loads are rarely constant power
EMT programs use numerical methods that are subject to conditioning and convergence errors, and numerical instability.
Grounding is often modeled explicitly.
Longer transmission lines typically decouple the model.
  Because there is not enough time for the signal to propagate down the line and back
Modeling decisions must be made based on the questions you are trying to answer.