## Slide 1: ECEN 616, Fall 2022 Methods of Electric Power System Analysis
Prof. Adam Birchfield
Dept. of Electrical and Computer Engineering
Texas A&M University
abirchfield@tamu.edu
Class 9: Numerical Methods for Transient Analysis, part 1

## Slide 2: What’s the Solution to this Differential Equation?
,
Analytical solution:
Numerical methods: solving successive time values separated by
  Euler, or Forward Euler, is the simplest explicit method
  Backward Euler, is the simplest implicit method
  Trapezoidal, implicit method sort of like an average of Forward and Backward Euler
  Runge-Kutta 2, explicit method based on further expansion of Taylor series
  Runge-Kutta 4, extended version of RK2
  Adams-Bashforth, a multi-step explicit method
  Other methods…
Euler’s method says:
  So for this example,
  Table on right shows for
t | Analytical | Euler
0 | 1 | 1
0.1 | 0.90484 | 0.90000
0.2 | 0.81873 | 0.81000
0.3 | 0.74082 | 0.72900
0.4 | 0.67032 | 0.65610
0.5 | 0.60653 | 0.59049
0.6 | 0.54881 | 0.53144

## Slide 3: Definition of Other Methods
Backward Euler, is the simplest implicit method
  Definition:
  This means we have to do some algebraic manipulation (implicit method)
  For our example:
  Solve for
Trapezoidal, implicit method averaging Forward and Backward Euler
  Definition:
  For our example:
  Solve again:
For both of these methods, we rely on being able to solve back for , which may not be easy for complicated non-linear functions
Theoretical error for any of these first three is

## Slide 4: Definition of Other Methods, Continued
Runge-Kutta 2, explicit method based on second-order approximation of Taylor series (considering as a function of both and )
(This is the same as Euler term)
Derivation of this is given on the next two slides, for reference.
Runge-Kutta 4, extended version of RK2 to the fourth-order polynomial

## Slide 5: Derivation of the Runge-Kutta 2nd Order Model
Take the Taylor series of out to the second order
Now try to find a method with the following form
Expand with a multi-variable Taylor series
Remember

## Slide 6: Derivation of the RK2, continued
Now plug in expanded version of k2 and k1
Comparing coefficients to the full Taylor series, we get
Arbitrarily choose and we get
Resulting formulation has error of
Similar derivation for fourth-order Runge-Kutta, with error
These are explicit methods, no need to solve algebraic equations

## Slide 7: Definition of Other Methods, Continued
Adams-Bashforth, a multi-step explicit method
  Definition:
  Notice it uses the prior time step
  This is good computationally since we should have this data already.
  But one issue is nonlinearities and discontinuities
  Error is order
There are many other methods, including Adams-Moulton, predictor-corrector, along with higher-order RK methods

## Slide 8: Summary of Methods
Name | Type | Error | Notes
Euler | Explicit |  | 
Backward Euler | Implicit |  | Because it is implicit, requires backsolving algebraic equations
Trapezoidal | Implicit |  | Because it is implicit, requires backsolving algebraic equations. Often better than backward Euler
Runge-Kutta 2 | Explicit |  | Requires differential equations be evaluated twice per time step
Runge-Kutta 4 | Explicit |  | Requires differential equations be evaluated four times per time step
Adams-Bashforth | Explicit |  | Uses prior time step solution, which may cause errors with discontinuities
Name | Type | Error | Notes
Euler | Explicit |  | 
Backward Euler | Implicit |  | Because it is implicit, requires backsolving algebraic equations
Trapezoidal | Implicit |  | Because it is implicit, requires backsolving algebraic equations. Often better than backward Euler
Runge-Kutta 2 | Explicit |  | Requires differential equations be evaluated twice per time step
Runge-Kutta 4 | Explicit |  | Requires differential equations be evaluated four times per time step
Adams-Bashforth | Explicit |  | Uses prior time step solution, which may cause errors with discontinuities
An advantage of implicit methods is they are numerically stable. But that doesn’t mean explicit methods wouldn’t be appropriate in many applications.

## Slide 9: Numerical Experiments
t | Analytical Solution | Euler | Backward Euler | Trapezoidal | Runge-Kutta 2 | Runge-Kutta 4 | Adams-Bashforth
0 | 1 | 1 | 1 | 1 | 1 | 1 | 1
0.1 | 0.904837 | 0.9 | 0.909091 | 0.904762 | 0.905 | 0.904838 | 0.9
0.2 | 0.818731 | 0.81 | 0.826446 | 0.818594 | 0.819025 | 0.818731 | 0.815
0.3 | 0.740818 | 0.729 | 0.751315 | 0.740633 | 0.741218 | 0.740818 | 0.73775
0.4 | 0.67032 | 0.6561 | 0.683013 | 0.670096 | 0.670802 | 0.67032 | 0.667838
0.5 | 0.606531 | 0.59049 | 0.620921 | 0.606278 | 0.607076 | 0.606531 | 0.604549
0.6 | 0.548812 | 0.531441 | 0.564474 | 0.548537 | 0.549404 | 0.548812 | 0.547259
0.7 | 0.496585 | 0.478297 | 0.513158 | 0.496295 | 0.49721 | 0.496586 | 0.495397
0.8 | 0.449329 | 0.430467 | 0.466507 | 0.449029 | 0.449975 | 0.449329 | 0.448451
0.9 | 0.40657 | 0.38742 | 0.424098 | 0.406264 | 0.407228 | 0.40657 | 0.405953
1 | 0.367879 | 0.348678 | 0.385543 | 0.367573 | 0.368541 | 0.36788 | 0.367483
1.1 | 0.332871 | 0.313811 | 0.350494 | 0.332566 | 0.33353 | 0.332871 | 0.332658
1.2 | 0.301194 | 0.28243 | 0.318631 | 0.300893 | 0.301844 | 0.301195 | 0.301133
1.3 | 0.272532 | 0.254187 | 0.289664 | 0.272236 | 0.273169 | 0.272532 | 0.272596
1.4 | 0.246597 | 0.228768 | 0.263331 | 0.246309 | 0.247218 | 0.246597 | 0.246763
1.5 | 0.22313 | 0.205891 | 0.239392 | 0.222851 | 0.223732 | 0.22313 | 0.223379
1.6 | 0.201897 | 0.185302 | 0.217629 | 0.201627 | 0.202478 | 0.201897 | 0.20221
1.7 | 0.182684 | 0.166772 | 0.197845 | 0.182425 | 0.183242 | 0.182684 | 0.183048
1.8 | 0.165299 | 0.150095 | 0.179859 | 0.165051 | 0.165834 | 0.165299 | 0.165701
1.9 | 0.149569 | 0.135085 | 0.163508 | 0.149332 | 0.15008 | 0.149569 | 0.149998
2 | 0.135335 | 0.121577 | 0.148644 | 0.13511 | 0.135822 | 0.135336 | 0.135783

## Slide 10: Error Analysis