## Slide 1: ECEN 460, Spring 2023 Power System Operation and Control
Prof. Adam Birchfield
Dept. of Electrical and Computer Engineering
Texas A&M University
abirchfield@tamu.edu
Class 11: Power Flow Examples

## Slide 2: Exam 1 Coming Up on 2/28/23
Covers new material through last week (this week is working example problems), labs, reading, homework, quizzes
You may have one 8.5"x11" sheet of paper, front and back, with handwritten notes to use during the exam
Includes conceptual material as well as being able to work problems
Exam big-picture topics:
  Power engineering fundamentals: ac circuits, complex power, three-phase
  Power system overview, operations, history, design practices, modeling concepts
  Generators
  Transformers and the per-unit system
  Transmission lines
  Newton-Raphson power flow

## Slide 3: Power Flow Bus Types
Each bus has one of three basic types, and for each one there are two known variables and two unknown variables:
  Load (PQ) bus
    Assume P/Q are fixed at most buses in the system
    Known: and , Unknown: and
  Slack bus
    Only one in the whole system
    Usually assigned to a large generator bus
    Known: and , Unknown: and
    Provides angle reference () and picks up the slack P
  Generator (PV) bus
    Other generators (5-10% of buses in a large system)
    Assume generator is controlling power output and voltage
    Known: and , Unknown: and

## Slide 4: Newton-Raphson Power Flow Procedure
Same procedure we have been using for N-R solutions so far
Build the Y-bus matrix
Write the list of variables and power balance equations
Make the power flow Jacobian
Make an initial guess of
While

## Slide 5: Power Flow Example #1
For the two bus power system shown below, use the Newton-Raphson power flow to determine the voltage magnitude and angle at bus two. Assume that bus one is the slack and SBase = 100 MVA.

## Slide 6: Power Flow Example #1

## Slide 7: Power Flow Example #1, Solution
For the two bus power system shown below, use the Newton-Raphson power flow to determine the voltage magnitude and angle at bus two. Assume that bus one is the slack and SBase = 100 MVA.

## Slide 8: Power Flow Example #1, Solution Cont.

## Slide 9: Two Bus Solved Values
Once the voltage angle and magnitude at bus 2 are known we can calculate all the other system values, such as the line flows and the generator reactive power output

## Slide 10: Low Voltage Solution!
This shows the region of convergence for different initial guesses of bus 2 angle (x-axis) and magnitude (y-axis)
Red region converges to the high voltage solution, while the yellow region converges to the low voltage solution

## Slide 11: Generator Reactive Power Limits
The reactive power output of generators varies to maintain the terminal voltage; on a real generator this is done by the exciter
To maintain higher voltages requires more reactive power
Generators have reactive power limits, which are dependent upon the generator's MW output
These limits must be considered during the power flow solution
  During power flow, once a solution is obtained, check to make generator reactive power output is within its limits
  If the reactive power is outside of the limits, fix Q at the max or min value, and resolve treating the generator as a PQ bus
    this is know as "type-switching"
    also need to check if a PQ generator can again regulate
Rule of thumb: to raise system voltage we need to supply more vars

## Slide 12: Power Flow Example #2
Bus 1 contains a large generating unit operating at V=1.0 pu
Bus 2 has a load consuming 200 MW and 100 MVR
Bus 3 has a generator that is set to produce 30 MW and control its terminal voltage to 1.0 pu
Want to solve for all bus voltages and line flows

## Slide 13: Power Flow Example #2

## Slide 14: Power Flow Example #2

## Slide 15: Power Flow Example #2

## Slide 16: Power Flow Example #2, Solution
First, figure out bus types, knowns, and unknowns
Build Y-bus
Identify variables and equations (unknown , V and known P, Q)
Bus | Type | Known | Unknown
1 | Slack | , V | P, Q
2 | PQ | P, Q | , V
3 | PV | P, V | , Q
Bus | Type | Known | Unknown
1 | Slack |  | P, Q
2 | PQ | P, Q | 
3 | PV | P, V | 
Y-bus=

## Slide 17: Power Flow Example #2, Solution
Write out power balance equations to get f(x):
And the Jacobian from all the partial derivatives
Bus | Type | Known | Unknown
1 | Slack | , V | P, Q
2 | PQ | P, Q | , V
3 | PV | P, V | , Q
Bus | Type | Known | Unknown
1 | Slack |  | P, Q
2 | PQ | P, Q | 
3 | PV | P, V | 
Y-bus=;

## Slide 18: Power Flow Example #2, Solution
Iteration 1
Iteration 2
Iteration 3

## Slide 19: The N-R Power Flow: 5-Bus Example
400 MVA
15 kV
400 MVA
15/345 kV
T1
T2
800 MVA
345/15 kV
800 MVA
15 kV
520 MVA
80 MW
40 Mvar
280 Mvar
800 MW
Line 3 345 kV
Line 2
Line 1
345 kV 100 mi
345 kV 200 mi
50 mi
1
4
3
2
5
Single-line diagram

## Slide 20: The N-R Power Flow: 5-Bus Example
Bus | Type | V per unit |  degrees | PG per unit | QG per unit | PL per unit | QL per unit | QGmax per unit | QGmin per unit
1 | Swing | 1.0 | 0 |  |  | 0 | 0 |  | 
2 | Load |  |  | 0 | 0 | 8.0 | 2.8 |  | 
3 | Constant voltage | 1.05 |  | 5.2 |  | 0.8 | 0.4 | 4.0 | -2.8
4 | Load |  |  | 0 | 0 | 0 | 0 |  | 
5 | Load |  |  | 0 | 0 | 0 | 0 |  | 
Table 1.
Bus input
data
Bus-to-Bus | R’ per unit | X’ per unit | G’ per unit | B’ per unit | Maximum MVA per unit
2-4 | 0.0090 | 0.100 | 0 | 1.72 | 12.0
2-5 | 0.0045 | 0.050 | 0 | 0.88 | 12.0
4-5 | 0.00225 | 0.025 | 0 | 0.44 | 12.0
Table 2.
Line input data
Notes: 20

## Slide 21: The N-R Power Flow: 5-Bus Example
Bus-to-Bus | R per unit | X per unit | Gc per unit | Bm per unit | Maximum MVA per unit | Maximum TAP Setting per unit
1-5 | 0.00150 | 0.02 | 0 | 0 | 6.0 | —
3-4 | 0.00075 | 0.01 | 0 | 0 | 10.0 | —
Table 3.
Transformer
input data
Bus | Input Data | Unknowns
1 | V1 = 1.0, 1 = 0 | P1, Q1
2 | P2 = PG2-PL2 = -8 Q2 = QG2-QL2 = -2.8 | V2, 2
3 | V3 = 1.05 P3 = PG3-PL3 = 4.4 | Q3, 3
4 | P4 = 0, Q4 = 0 | V4, 4
5 | P5 = 0, Q5 = 0 | V5, 5
Table 4. Input data
and unknowns
Notes: 21

## Slide 22: Time to Close the Hood: Let the Computer Do the Math! (Ybus Shown)
Notes: 22

## Slide 23: Ybus Details
Elements of Ybus connected to bus 2
Notes: 23

## Slide 24: Here Are the Initial Bus Mismatches
Notes: 24

## Slide 25: And the Initial Power Flow Jacobian
Notes: 25

## Slide 26: And the Hand Calculation Details!
Notes: 26

## Slide 27: Five Bus Power System Solved
Notes: 27

## Slide 28: Five Bus System with Capacitor
A capacitor has been added at bus 2 to fix its low voltage

## Slide 29: Contingency Analysis
Contingency analysis provides an automatic way of looking at all the statistically likely contingencies. In this example the contingency set is all the single line and transformer outages
Notes: 29

## Slide 30: Power Flow Application - PJM Control Center
Their generation capacity is about 177 GW