## Slide 1: ECEN 460, Spring 2023 Power System Operation and Control
Prof. Adam Birchfield
Dept. of Electrical and Computer Engineering
Texas A&M University
abirchfield@tamu.edu
Class 18: Economic Dispatch, Part 2

## Slide 2: Homework
Homework due next class:
  6th edition: Problems 6.62, 6.63, 6.65
  7th edition: Problems 7.1, 7.2, 7.4
The next few quizzes will be on economic dispatch
Generator paper due in 1 week, April 4th

## Slide 3: Steam Plant (Coal)
Source: Masters, Renewable and Efficient Electric Power Systems, 2004

## Slide 4: Natural Gas Simple Cycle and Combined Cycle
Simple Cycle
Typical efficiency is around 30 to 35%
Combined Cycle
Efficiencies of up to 60% can be achieved, with even higher values when the steam is used for heating. Fuel is usually natural gas

## Slide 5: Variation in Natural Gas Prices
Our Feb 14, 2021 event set a 12-year record. Marginal cost for natural gas fired electricity price in $/MWh is about 7-10 times gas price.
Source: EIA

## Slide 6: Mathematical Formulation of Costs
Generator cost curves are usually not smooth. However the curves can usually be adequately approximated using piece-wise smooth, functions.
Two representations predominate
  quadratic or cubic functions
  piecewise linear functions
In 460 we’ll generally assume a quadratic representation

## Slide 7: Incremental Cost Example
Then

## Slide 8: Economic Dispatch Problem
The goal of economic dispatch is to determine the generation dispatch that minimizes the instantaneous operating cost, subject to the constraint that total generation = total load + losses
System total cost
Cost for generator as a function of the generator's real power
Total system power demand

## Slide 9: Unconstrained Minimization
This is a minimization problem with a single equality constraint
For an unconstrained minimization a necessary (but not sufficient) condition for a minimum is the gradient of the function must be zero,
The gradient generalizes the first derivative for multi-variable problems:

## Slide 10: Minimization with Equality Constraint
When the minimization is constrained with an equality constraint we can solve the problem using the method of Lagrange Multipliers
Key idea is to modify a constrained minimization problem to be an unconstrained problem
:

## Slide 11: Economic Dispatch Lagrangian
For generators not at their limits, the incremental cost is equal to

## Slide 12: Economic Dispatch Example
Calculate the economic dispatch for a two-generator system:

## Slide 13: Economic Dispatch Example Solution
Calculate the economic dispatch for a two-generator system:
Using the Lagrange multiplier method we know

## Slide 14: Economic Dispatch Example Solution, Cont’d

## Slide 15: Worksheet -- Economic Dispatch, Exercise 2
Four generators with the following cost equations and limits:
Two parts to this question:
Make a table with five values of (system marginal cost): 9, 12, 15, 18, 21 $/MWh. Calculate and total system P for each of these ’s. (Remember, for each generator i not at a limit.)
If we want to serve a total of 500 MW of load, what is the optimal dispatch (), the system marginal cost , and total cost?

## Slide 16: Economic Dispatch, Exercise 2
($/MWh) |  |  |  |  | 
9 |  |  |  |  | 
12 |  |  |  |  | 
15 |  |  |  |  | 
18 |  |  |  |  | 
21 |  |  |  |  | 
9 |  |  |  |  | 
12 |  |  |  |  | 
15 |  |  |  |  | 
18 |  |  |  |  | 
21 |  |  |  |  | 

## Slide 17: Lambda-Iteration Solution Method
The direct solution only works well if the incremental cost curves are linear and no generators are at their limits
A more general method is known as the lambda-iteration
  the method requires that there be a unique mapping between a value of lambda and each generator’s MW output
  the method then starts with values of lambda below and above the optimal value, and then iteratively brackets the optimal value

## Slide 18: Lambda-Iteration Algorithm

## Slide 19: Lambda-Iteration: Graphical View
In the graph shown, for each value of lambda
there is a unique PGi for each generator. This
relationship is the PGi() function.

## Slide 20: Lambda-Iteration Example

## Slide 21: Lambda-Iteration Example

## Slide 22: Lambda-Iteration Example, Cont’d

## Slide 23: Lambda-Iteration Example, Cont’d

## Slide 24: Lambda-Iteration Example, Cont’d