## Slide 1: ECEN 460, Spring 2023 Power System Operation and Control
Prof. Adam Birchfield
Dept. of Electrical and Computer Engineering
Texas A&M University
abirchfield@tamu.edu
Class 20: Introduction to Power System Dynamics

## Slide 2: Homework
Generator paper due today on Canvas (ok to submit up to midnight)

## Slide 3: ERCOT Nodal Market Overview
Image source: ERCOT market education, transmission 101

## Slide 4: ERCOT Market Relationships
Image source: ERCOT market education, transmission 101
LSE is load serving entity; QSE is qualified scheduling entity

## Slide 5: Class Outline
Review of three-phase AC power calculations
Structure, history, and design of power systems
Generator and load modeling
Transmission line and transformer modeling
The power flow problem and solution methods
Economic power system operation
Dynamics and stability of power systems
Emerging topics
✔
✔
✔
✔
✔
✔
➔
Exam 2 will focus on these topics
Tuesday, April 18
A bit more conceptual material between Exam 2 and the final

## Slide 6: Exam 2 – Tuesday April 18th
Conceptual questions:
  Newton-Raphson Power flow
  Power flow approximations (such as DC power flow)
  Large power system operations (such as the 24 statements)
  Power system economics (economic dispatch, OPF, SCOPF, markets)
  Dynamics and stability (what we’re starting today). No problems related to dynamics for Exam 2, but the Final will likely have a dynamics problem.
One problem related to power flow (including full Newton-Raphson power flow and/or DC power flow)
One problem related to economic dispatch

## Slide 7: Example of Frequency Variation
Figure shows Eastern Interconnect frequency variation after loss of 2600 MW

## Slide 8: Example of Dynamics Behavior
Source: August 14th 2003 Blackout Final Report

## Slide 9: Power System Dynamics Motivation: Frequency Decline September 2011 Blackout
Image Source: Arizona-Southern California Outages on September 8, 2011 Report, FERC and NERC, April 2012

## Slide 10: Power Grid Disturbance Example
Time in seconds
Figures show the frequency change as a result of the sudden loss of a large amount of generation in the Southern WECC
Frequency contour
Green is bus quite close to location of generator trip while blue and red are quite distant.
Frequency in HZ

## Slide 11: Recap: Power Flow
The power flow is used to determine a quasi steady-state operating condition for a power system
  Goal is to solve a set of algebraic equations
    g(y) = 0 [y variables are bus voltage and angle]
  Models employed reflect the steady-state assumption
  Using a power flow, after a contingency occurs (such as opening a line), the algebraic equations are solved to determine a new equilibrium

## Slide 12: Power Flow vs. Dynamics
Dynamic simulations are used to determine whether following a contingency the power system returns to a steady-state operating point
  Goal is to solve a set of differential and algebraic equations,
    dx/dt = f(x,y) [y variables are bus voltage and angle]
    g(x,y) = 0 [x variables are dynamic state variables]
  Starts in steady-state, and hopefully returns to a usually new steady-state value
  Models reflect the transient stability time frame (up to dozens of seconds)
    Slow Values  Treat as constants
    Ultra Fast States  Treat as algebraic relationships

## Slide 13: Power System Transient Stability
In order to operate as an interconnected system all of the generators (and other synchronous machines) must remain in synchronism with one another
  Synchronism requires that (for two pole machines) the rotors turn at exactly the same speed
Loss of synchronism results in a condition in which no net power can be transferred between the machines
A system is said to be transiently unstable if following a disturbance one or more of the generators lose synchronism

## Slide 14: Power System Time Scales and Transient Stability
Image source: P.W. Sauer, M.A. Pai, Power System Dynamics and Stability, 1997, Fig 1.2, modified

## Slide 15: Power System Stability Terms
Terms continue to evolve, but a good reference is [1]; image shows Figure 1 from this reference
[1] IEEE/CIGRE Joint Task Force on Stability Terms and Definitions, “Definitions and Classification of Power System Stability,” IEEE Transactions Power Systems, May 2004, pp. 1387-1401

## Slide 16: Differential Algebraic Equations (DAEs)
Simple example
Initial value problem (IVP): we know the starting value of , we want to determine it for future time.
This one is separable, and an analytical solution is possible: exponential decay.
In general, with as a vector of many differentials

## Slide 17: Power System Dynamics DAEs
Example power system problem with differential algebraic equations (DAEs) is the classical synchronous generator connected to an infinite bus.
The two differential variables are and ; in practice dynamic models can have many more.

## Slide 18: Handout Example
Assume we have the following differential equations ()
With the following data:
, , , , , ,
Rewrite these differential equations just in terms of and
2. What are the two equilibrium points of this system? (Hint: a set of differential equations will be at equilibrium when they are not changing with time, that is, all time derivatives are zero.)

## Slide 19: Solving DAEs
General form:
  We will consider the simpler case without , the additional algebraic variables:
  We need the initial value of , which is either given or found from an equilibrium point, where
  Higher-order systems can be put in this form
Except for special cases, such as linear systems, an analytic solution is usually not possible – numerical methods must be used

## Slide 20: Solving DAEs Numerically
Numerical solution methods do not generate exact solutions; they practically always introduce some error
  Methods assume time advances in discrete increments, called a stepsize (or time step), Dt
  Speed accuracy tradeoff: a smaller Dt usually gives a better solution, but it takes longer to compute
  Numeric round-off error due to finite floating point arithmetic
A solution exists as long as is continuously differentiable

## Slide 21: Error Propagation
At each time step the total round-off error is the sum of the local round-off at time and the propagated error from steps 1, 2 , … , k − 1
An algorithm with the desirable property that local round-off error decays with increasing number of steps is said to be numerically stable
Otherwise, the algorithm is numerically unstable
Numerically unstable algorithms can nevertheless give quite good performance if appropriate time steps are used
  This is particularly true when coupled with algebraic equations

## Slide 22: Euler’s Method
The simplest technique for numerical integration is known as the forward Euler’s method.
Approximate as
Then
Each step of depends only on the previous value
only needs to be evaluated once.
Typically, smaller gives better approximations.

## Slide 23: Euler’s Method Algorithm
Set (usually 0)
Pick a time step , which is problem specific
While Do
End While

## Slide 24: Handout Example
Fill out the following table for this system starting at the given point, using Euler’s method with a time step of 0.01 seconds. Try it on a spreadsheet or with a script out to 2 seconds. Is the system stabilizing to an equilibrium point?
t |  |  |  | 
0 | 0.4 | 0 |  | 
t |  |  |  | 
0 | 0.4 | 0 |  | 

## Slide 25: Solution to Handout Example
Yes, it is stabilizing to the first equilibrium point

## Slide 26: Runge-Kutta Methods
Runge-Kutta methods improve on Euler's method by evaluating at selected points within the time step
Simplest method is the second order method (RK2)
is what we get from Euler's; improves on this by reevaluating at the estimated end of the step
RK2 must evaluate twice at each times step.

## Slide 27: Other Numerical Solution Methods
One-step methods: require information about solution just at one point,
  Forward Euler and Runge-Kutta fall in this category
Multi-step methods: make use of information at more than one point, , , …
  Adams-Bashforth
Predictor-Corrector Methods: implicit
  Backward Euler

## Slide 28: Example #1
First problem has one variable and known analytical solution.
Choose timestep of 0.1
First time point after initial is
Next time point:

## Slide 29: Example #1, Cont.
 | Actual | Euler | Euler 05 | Runge-Kutta 2
0 | 10 | 10 | 10 | 10
0.1 | 9.048 | 9 | 9.02 | 9.050
0.2 | 8.187 | 8.10 | 8.15 | 8.190
0.3 | 7.408 | 7.29 | 7.35 | 7.412
… | … | … | … | …
1.0 | 3.678 | 3.49 | 3.58 | 3.685
… | … | … | … | …
2.0 | 1.353 | 1.22 | 1.29 | 1.358
 | Actual |  |  | 
0 | 10 | 10 | 10 | 10
0.1 | 9.048 | 9 | 9.02 | 9.050
0.2 | 8.187 | 8.10 | 8.15 | 8.190
0.3 | 7.408 | 7.29 | 7.35 | 7.412
… | … | … | … | …
1.0 | 3.678 | 3.49 | 3.58 | 3.685
… | … | … | … | …
2.0 | 1.353 | 1.22 | 1.29 | 1.358

## Slide 30: Example #2
Consider the equations describing the horizontal position of a cart attached to a lossless spring:
Initial conditions and
Analytical solution is
Numerical solution:
Choose step size of 0.25

## Slide 31: Example #2, Cont.
Starting from the initial conditions at t=0 we next calculate the value of at .
Then we continue to the next time step, t=0.5

## Slide 32: Example #2, Cont.
t | x1actual(t) | x1(t) Dt=0.25
0 | 1 | 1
0.25 | 0.9689 | 1
0.50 | 0.8776 | 0.9375
0.75 | 0.7317 | 0.8125
1.00 | 0.5403 | 0.6289
… | … | …
10.0 | -0.8391 | -3.129
100.0 | 0.8623 | -151,983
Since we know from the exact solution that x1 is bounded between -1 and 1, clearly the method is numerically unstable

## Slide 33: Example #2, Cont.
Dt | x1(10)
actual | -0.8391
0.25 | -3.129
0.10 | -1.4088
0.01 | -0.8823
0.001 | -0.8423
Below is a comparison of the solution values for x1(t)
at time t = 10 seconds

## Slide 34: Generator Transient Stability Models
In order to study the transient response of a power system we need to develop models for the generator valid during the transient time frame of several seconds following a system disturbance
We need to develop both electrical and mechanical models for the generators

## Slide 35: Generator Electrical Model
The simplest generator model, known as the classical model, treats the generator as a voltage source behind the direct-axis transient reactance; the voltage magnitude is fixed, but its angle changes according to the mechanical dynamics

## Slide 36: Generator Mechanical Model
Generator Mechanical Block Diagram

## Slide 37: Generator Mechanical Model, Cont’d
In general power = torque x angular speed
Hence, when a generator is spinning at speed
Initially we'll assume no damping (.
Then
is the mechanical power input, which is assumed initially to be constant throughout the study time period.

## Slide 38: Generator Mechanical Model, Cont’d

## Slide 39: Generator Mechanical Model, Cont’d

## Slide 40: Generator Swing Equation

## Slide 41: Single Machine Infinite Bus (SMIB)
To understand the transient stability problem we’ll first consider the case of a single machine (generator) connected to a power system bus with a fixed voltage magnitude and angle (known as an infinite bus) through a transmission line with impedance jXL

## Slide 42: SMIB, Cont’d

## Slide 43: SMIB Equilibrium Points

## Slide 44: Transient Stability Analysis
For transient stability analysis we need to consider three systems
  Prefault - before the fault occurs the system is assumed to be at an equilibrium point
  Faulted - the fault changes the system equations, moving the system away from its equilibrium point
  Postfault - after fault is cleared the system hopefully returns to a new operating point
Actual transient stability studies can have multiple events

## Slide 45: Transient Stability Solution Methods
There are two methods for solving the transient stability problem
  Numerical integration
    this is by far the most common technique, particularly for large systems; during the fault and after the fault the power system differential equations are solved using numerical methods
  Direct or energy methods; for a two bus system this method is known as the equal area criteria
    mostly used to provide an intuitive insight into the transient stability problem

## Slide 46: SMIB Example
Assume a generator is supplying power to an infinite bus through two parallel transmission lines. Then a balanced three phase fault occurs at the terminal of one of the lines. The fault is cleared by the opening of this line’s circuit breakers.

## Slide 47: SMIB Example, Cont’d
Simplified prefault system

## Slide 48: SMIB Example, Faulted System
During the fault the system changes
The equivalent system during the fault is then
During this fault no
power can be transferred
from the generator to
the system

## Slide 49: SMIB Example, Post Fault System
After the fault the system again changes
The equivalent system after the fault is then

## Slide 50: SMIB Example, Dynamics