## Slide 1: ECEN 615, Fall 2023 Methods of Electric Power System Analysis
Prof. Adam Birchfield
Dept. of Electrical and Computer Engineering
Texas A&M University
abirchfield@tamu.edu
Class 3: Power Calculations Review

## Slide 2: Announcements
Get PowerWorld installed
Watch the videos on the website if you need more background review
RSVP to the EPG dinner if you’d like to join
Distance students, send your paragraphs for class discussion to me by email by 5pm Mondays for the prior week. If you haven’t sent last weeks, go ahead and send it by tomorrow.

## Slide 3: Power Systems Operate on Many Time Scales
Slide source: Prof. George Gross UIUC ECE 530

## Slide 4: Power Systems Operate on Many Time Scales
Slide source: Prof. George Gross UIUC ECE 530

## Slide 5: Power System Operation Regimes
Slide source: Prof. George Gross UIUC ECE 530

## Slide 6: Generation Control and Scheduling Example
Slide source: Prof. George Gross UIUC ECE 530

## Slide 7: Static Power System Analysis
One of the most common power system analysis tools is the power flow, which tells how power flows through a power system in the quasi-steady state time frame
  Load flow is an alternative name for power flow; both terms have been used interchangeably for at least 50 years. I prefer power flow because the power flows, not the load
The power flow can be used to model the full, three-phase system, but usually (practically always) for transmission system analysis the system is assumed to be balanced. Hence a per phase equivalent model is used.

## Slide 8: Exercise: Solve This Circuit
How do we solve this DC circuit for different values of P?
P | Load voltage and current | 
0 W |  | 
1 W |  | 
2 W |  | 
4 W |  | 
5 W |  | 
6 W |  | 
10 W |  | 

## Slide 9: Exercise: Problem 1
The current through an impedance is A. The impedance consists of a resistor in series with a mH inductor. Assume the system is operated at 60 Hz. What are the real power and reactive power consumed by this element?
A transmission bus voltage, measured from phase a to phase b, is . What is the phase a to neutral voltage? Assume system is operated in a-b-c phase sequence. Give the answer both as a phasor and as a cosine-based time function.
A load draws 200 kW with a lagging pf of 0.8. What is the reactive power drawn by the load?

## Slide 10: Workspace

## Slide 11: Workspace

## Slide 12: Workspace

## Slide 13: Exercise: Problem 2
A three-phase power system consists of four buses. There is a generator at bus 1 operating at voltage . There is a load at bus 4 consuming 18 + j4 MVA. Between buses 1 and 2 there is a 13.8 kV : 138 kV transformer with impedance j0.1 on the bus 1 side. There is a 138 kV transmission line connecting buses 2 and 3 with series impedance 3 + j8 and shunt capacitance with admittance j200 . There is a 138 kV : 69 kV transformer between buses 3 and 4 with impedance j10 on the bus 3 side.
Draw a one-line diagram of this system
Write out the table of per-unit bases
Convert all the values given above to per-unit
Write the y-bus matrix for this system

## Slide 14: Workspace

## Slide 15: Workspace

## Slide 16: Workspace

## Slide 17: Workspace

## Slide 18: Exercise: Problem 3
For a two-bus system, bus 1 is the slack generator bus with . Bus 2 is a PQ bus with a constant power load of and . A branch connects the two buses with series impedance .
Starting with an initial guess of , use the Newton-Raphson power flow method to obtain the load bus voltage angle and magnitude after two iterations.

## Slide 19: Workspace

## Slide 20: Workspace

## Slide 21: Reference Notes from the Videos

## Slide 31: The Power Flow Problem
What we know:
  Generator real power
  Generator voltage magnitude
  Load real and reactive power
What we don't know:
  Bus voltage angles
  Non-generator bus voltage magnitude
  Generator reactive power
  Current injections of generators or loads
Note that the problem is formulated with power values, not current, so we cannot use the Y-bus equations directly
Power flow problem is non-linear

## Slide 33: Power Flow Problem Variables
These two equations must be satisfied for all buses in the system
Total of 2n equations
Parameters g and b are known from the Y-bus
Each bus has four variables:
  Bus voltage magnitude
  Bus voltage angle
  Bus real power injection
  Bus reactive power injection
So in general, we need to pre-specify 2 additional variables at each bus before we can solve

## Slide 34: Power Flow Bus Types
  Each bus has one of three basic types, and for each one there are two known variables and two unknown variables:
Load (PQ) bus
  Assume P/Q are fixed at most buses in the system
  Known: and , Unknown: and
Slack bus
  Only one in the whole system
  Usually assigned to a large generator bus
  Known: and , Unknown: and
  Provides angle reference () and picks up the slack P
Generator (PV) bus
  Other generators (5-10% of buses in a large system)
  Assume generator is controlling power output and voltage
  Known: and , Unknown: and

## Slide 35: Newton-Raphson Method
Method:
Write equation as f()=0
Make an initial guess of ,
For iteration , define
Write Taylor series expansion:
Approximate with only first two terms:
Solve for
Solve for new estimate of

## Slide 36: Multi-Variable Newton-Raphson
Next, we generalize to the case where is an n-dimension vector, and f(x)=0 is an n-dimensional function
Again, define
Taylor series for

## Slide 37: Jacobian Matrix
We can write the truncated Taylor series in Matrix form as the Jacobian matrix
So,
And so

## Slide 38: Multi-Variable Newton-Raphson Example
Solve for and such that