## Slide 1: ECEN 615, Fall 2023 Methods of Electric Power System Analysis
Prof. Adam Birchfield
Dept. of Electrical and Computer Engineering
Texas A&M University
abirchfield@tamu.edu
Class 17: State Estimation, Part 2

## Slide 2: Discussion: “Digital Twin”

## Slide 3: DC State Estimation Example Solution
State estimation solution: ,
Measurement | Value
 | 103.5 MW
 | 83.8 MW
 | 51.4 MW
 | 183.4 MW
 | 53.3 MW
 | 130.8 MW
Measurement | Value
 | 103.5 MW
 | 83.8 MW
 | 51.4 MW
 | 183.4 MW
 | 53.3 MW
 | 130.8 MW
Assume , ,

## Slide 4: SE Observability
In order to estimate all n states we need at least n measurements. However, where the measurements are located is also important, a topic known as observability
  In order for a power system to be fully observable usually we need to have a measurement available no more than one bus away
  At buses we need to have at least measurements on all the injections into the bus except one (including loads and gens)
  Loads are usually flows on feeders, or the flow into a transmission to distribution transformer
  Generators are usually just injections from the GSU

## Slide 5: Pseudo Measurements
Pseudo measurements are used at buses in which there is no load or generation; that is, the net injection into the bus is know with high accuracy to be zero
  In order to enforce the net power balance at a bus we need to include an explicit net injection measurement
To increase observability sometimes estimated values are used for loads, shunts and generator outputs
  These “measurements” are represented as having a higher much standard deviation

## Slide 6: SE Bad Data Detection
The quality of the measurements available to an SE can vary widely, and sometimes the SE model itself is wrong. Causes include
  Modeling Errors: perhaps the assumed system topology is incorrect, or the assumed parameters for a transmission line or transformer could be wrong
  Data Errors: measurements may be incorrect because of in correct data specifications, like the CT ratios or even flipped positive and negative directions
  Transducer Errors: the transductors may be failing or may have bias errors
  Sampling Errors: SCADA does not read all values simultaneously and power systems are dynamic

## Slide 7: SE Bad Data Detection
The challenge for SE is to determine when there is likely a bad measurement (or multiple ones), and then to determine the particular bad measurements
J(x) is random number, with a probability density function (PDF) known as a chi-squared distribution, 2(K), where K is the degrees of freedom, K=m-n
It can be shown the expected mean for J(x) is K, with a standard deviation of
  Values of J(x) outside of several standard deviations indicate possible bad measurements, with the measurement residuals used to track down the likely bad measurements
SE can be re-run without the bad measurements

## Slide 8: Example SE Application: PJM and MISO
PJM provides information about their EMS model in
  www.pjm.com/-/media/documents/manuals/m03a.ashx
Data here is from the Sept 2018 (Rev 16) document

## Slide 9: Example SE Application: PJM and MISO
PJM measurements are required for 69 kV and up
PJM SE is triggered to execute every minute
PJM SE solves well over 98% of the time
Below reference provides info on MISO SE from March 2015
  54,433 buses
  54,415 network branches
  6332 generating units
  228,673 circuit breakers
  289,491 mapped points
https://www.naspi.org/sites/default/files/2017-05/3a%20MISO-NASPIWokshop-Synchrophasor%20Data%20and%20State%20Estimation.pdf

## Slide 10: Energy Management Systems (EMSs)
EMSs are now used to control most large scale electric grids
EMSs developed in the 1970’s and 1980’s out of SCADA systems
  An EMS usually includes a SCADA system; sometimes called a SCADA/EMS
Having a SE is almost the definition of an EMS. The SE then feeds data to the more advanced functions
EMSs have evolved as the industry as evolved as the industry has evolved, with functionality customized for the application (e.g., a reliability coordinator or a vertically integrated utility)

## Slide 11: NERC Reliability Coordinators
Source: www.nerc.com/pa/rrm/TLR/Pages/Reliability-Coordinators.aspx

## Slide 12: EEI Member Companies

## Slide 13: Electric Coops

## Slide 14: Texas Electric Coops

## Slide 15: ERCOT Control Center with EMS
Courtesy of ERCOT

## Slide 16: ERCOT EMS
Slide source: ERCOT, D. Penney, J. Mandavilli, M. Henry, “Loss of SCADA, EMS or LCC”

## Slide 17: ERCOT EMS

## Slide 18: SE Iterative Solution Algorithm
We make an initial guess of x, x(0) and iterate, calculating Dx each iteration
H is the partial derivatives
R is the measurement standard deviations
This is exactly the least squares form developed earlier with HTR-1H an n by n matrix. This could be solved with Gaussian elimination, but this isn't preferred because the problem is often ill-conditioned
Keep in mind that H is no longer constant, but varies as x changes. often ill-conditioned

## Slide 19: Example: Two Bus Case
Assume a two bus case with a generator supplying a load through a single line with x=0.1 pu. Assume measurements of the p/q flow on both ends of the line (into line positive), and the voltage magnitude at both the generator and the load end. So B12 = B21=10.0
We need to assume a reference angle unless we directly measuring phase

## Slide 20: Example: Two Bus Case
Let
We assume an angle reference of q1=0

## Slide 21: Example: Two Bus Case
With a flat start guess we get

## Slide 22: Example: Two Bus Case

## Slide 23: QR Factorization
Used in in SE since it handles ill-conditioned m by n matrices (with m >= n)
Can be used with sparse matrices
As before we will first split the R-1 matrix
QR factorization represents the m by n H' matrix as with Q an m by m orthonormal matrix and U an upper triangular matrix (most books use Q R but we use U to avoid confusion with the previous R)

## Slide 24: QR Factorization
We then have
But since Q is an orthonormal matrix,
Hence we have
Q is an m by m matrix

## Slide 25: QR Factorization
When factored the U matrix (i.e., what most call the R matrix) will be an m by n upper triangular matrix
Several methods are available
  The Householder method
    See Prof. Tim Davis’s book for sparse matrix QR factorization
  The Givens Method
    Givens can often be faster when dealing with sparse matrices
    A good reference is Gene H. Golub and Charles F. Van Loan, “Matrix Computations,” second edition, Johns Hopkins University Press, 1989.
    For a full matrix, Givens is O(mn2) since each element in the lower triangle needs to be zeroed O(nm), and each operation is O(n)
The QR factorization (Householder or Givens) is often used to solve State Estimation problems for power systems

## Slide 26: Assignment 5
Assignment 5 has to do with mixed-integer optimization using Python or Matlab with Gurobi (or another optimization platform)
You’ll be solving a unit commitment problem, which we’ll discuss in class next time.
For next class:
  Read through the assignment instructions
  Install and license Gurobi according to the instructions
  Set it up for Matlab or Python according to the instructions
  Run the example Matlab or Python case I provided you
  Bring your laptop to class
We’ll have some time in class to work on this assignment (last one of the semester!)
Due date: November 20th, 2023 at 4pm