## Slide 1: ECEN 460, Spring 2026 Power System Operation and Control
Prof. Adam Birchfield
Dept. of Electrical and Computer Engineering
Texas A&M University
abirchfield@tamu.edu
Class 2: Power System Structure and History

## Slide 2: Reminders
Review these topics
  Complex number math – by hand and calculator
  Phasors – representing AC voltage and current
  Impedance – for AC circuit solving
  Complex power – including power factor, reactive power
  Three phase – wye/delta, line-to-line/line-to-neutral voltage, per-phase analysis
Homework #1 and #2 are practice problems on these topics
  Homework #1 due next Tuesday (Jan 20) and Homework #2 due Tuesday Jan 27
Take advantage of the textbook, and office hours (me and TAs)
We’re going to have quizzes most classes to review

## Slide 3: Energy and Power
Energy is A property of matter that quantifies its ability to perform useful work.
  Forms: kinetic, gravitational, heat, light, sound, magnetic, nuclear, chemical, and electric
  Units for energy: 1 MWh = 1000 kWh 1 kWh = 3.6 million Joules = 3412.14 Btu
Power is Energy on the move from form to form or place to place.
  Time derivative of energy as it is transferred
  Units for power: Watt (Volt-Ampere) kW = 1000 W, MW, GW, 1 Hp = 746 Watts
One gallon of gasoline has about 0.125 MBtu (36.5 kWh) of energy stored in chemical form
U.S. annual electric energy consumption is about 3600 billion kWh
  This is about 13,333 kWh per person, which means on average we each use 1.5 kW of power continuously
Installed U.S. generation capacity is about 1000 GW (about 3 kW per person)
Maximum load of Bryan/College Station is about 500 MW

## Slide 4: Electric Power Systems
Electricity has many advantages for delivering the energy used by humankind
  Conversion to and from other forms is convenient and efficient (such as motors and generators)
  Transmission in bulk can be done quickly and efficiently over long distances (power lines)
  About 40% of U.S. energy consumption is electric
Power systems range in size
  Large: four major interconnections in North America
  Medium: islands, militarily installations, ships
  Small: airplanes, automobiles, portable battery systems

## Slide 5: Alternating Current Power Systems
Alternating current (ac) systems have sinusoidal voltage and current wave forms, as opposed to direct current (dc)
Small, battery-based systems such as automobiles are typically dc, and historically some larger systems have used dc
Ac is nearly exclusively used now for medium and large power system
  Better performance of motors and generators
  Allows use of transformers to step-up voltage for efficient long-distance transmission
Time (s)
Voltage (V)

## Slide 6: Choosing the AC Frequency
Lower frequency systems (10-40 Hz) require larger motors and transformers and can introduce flicker in some lighting technologies.
  These historically were used some for railroads
Higher frequency systems (100 Hz – 1 kHz) have higher voltage drops over long distances and can introduce more audible noise
  400 Hz is common in airplanes and spaceships, where weight is a primary consideration
Today, most large power systems use 50 or 60 Hz (60 Hz is used in the USA)
60 Hz
North America, about half of South America, half of Japan, a few other countries
50 Hz
Europe, most of Africa and Asia, part of South America

## Slide 7: The Far Past: Origins of the Electric Grid
First practical use of electricity 1860s-70s, mainly telegraph and lighting
1880s – Edison dc system in Manhattan, Westinghouse/Tesla ac system, invention of practical motors and transformers
1890s-1920s – Local three-phase ac systems (mainly coal and hydro) develop and expand to become large interstate holding companies
1930s-40s – Industry standardizes on 60 Hz ac (in the US), load growth with air conditioning, rural electrification and big hydro projects with the New Deal
1950s-60s – Interconnection into major grids
Santa Ana River 33 kV Line, circa 1899. This was the longest power line in the world at the time at 83 miles. (SCE Photograph, from The Grid by Julie Cohn)

## Slide 8: Major Grids in North America
Eastern Interconnect (EI)
Western Interconnect (WECC)
  EI and WECC were briefly interconnected in the 1970s
Texas Interconnect (ERCOT)
  Connected to East and Mexico with small AC-DC-AC interties
Quebec Interconnect
Smaller “island” grids in various places like Alaska and Hawaii

## Slide 9: The Three US Grids are All in Texas
Source: www.puc.texas.gov/industry/maps/maps/ERCOT.pdf

## Slide 10: Balanced Three-Phase () Systems
A balanced three-phase () system has
  three voltage sources with equal magnitude, but with an angle shift of 120
  equal loads on each phase
  equal impedance on the lines connecting the generators to the loads
Bulk power systems are almost exclusively 3
Single-phase is used primarily only in low voltage, low power settings, such as residential and some commercial

## Slide 11: Balanced 3 -- No Neutral Current
+
–
–
+
–
+
Phase “a”
Phase “c”
Neutral “n”
Phase “b”

## Slide 12: Advantages of 3 Power
Can transmit more power for same amount of wire (twice as much as single phase)
Torque produced by 3 machines is constant
Three-phase machines use less material for same power rating
Three-phase machines start more easily than single-phase machines

## Slide 13: Vertical Monopolies
Within a particular geographic market, the electric utility had an exclusive franchise
Generation
Transmission
Distribution
Customer Service
In return for this exclusive
franchise, the utility had the
obligation to serve all
existing and future customers
at rates determined jointly
by utility and regulators
It was a “cost plus” business

## Slide 14: Vertical Monopolies, 2
Within its service territory each utility was the only game in town
Neighboring utilities functioned more as colleagues than competitors
Utilities gradually interconnected their systems so by 1970 transmission lines crisscrossed North America, with voltages up to 765 kV
Economies of scale keep resulted in decreasing rates, so most every one was happy

## Slide 15: The More Recent Past – Restructuring
1970’s brought inflation, increased fossil-fuel prices, calls for conservation and growing environmental concerns
Increasing rates replaced decreasing ones
As a result, U.S. Congress passed Public Utilities Regulator Policies Act (PURPA) in 1978, which mandated utilities must purchase power from independent generators located in their service territory (modified 2005)
Major opening of industry to competition occurred as a result of National Energy Policy Act of 1992, mandating that utilities provide “nondiscriminatory” access to the high voltage transmission
Result over the last few years has been a dramatic restructuring of electric utility industry
Energy Bill 2005 repealed PUHCA; modified PURPA

## Slide 16: August 14th, 2003 Blackout
Above image from energy.gov, August 14, 2003 Blackout Final Report

## Slide 17: The Present: Changing Generation Mix
Fuel Source | 2024 US Electric Usage | Change from 2023 to 2024 | Change from 2014 to 2024
Coal | 21.4 % | - 3 % | - 57 %
Natural Gas | 42.5 % | + 4 % | + 66 %
Petroleum | 0.5 % | - 6 % | - 44 %
Nuclear | 25.0 % | + 1 % | - 2 %
Hydro | 2.5 % | - 1 % | - 6 %
Solar | 2.3 % | + 33 % | + 1164 %
Wind | 4.7 % | + 7 % | + 149 %
Source: US EIA Monthly Energy Review, December 2025

## Slide 18: The Present: Changing Generation Mix, 2
Texas is #1 in wind energy, with over 42,000 MW installed
Retirements in Texas from 2014-2024 included 7411 MW of coal, 5950 MW of natural gas, and small amounts of others
Generation listed as “proposed” for 2025-2030 includes 7120 MW natural gas, 5812 MW wind, 43,704 MW solar, plus 32,244 MW batteries
Source: US EIA Monthly Energy Review, EIA annual energy outlook, ERCOT, EIA 860

## Slide 19: The Future: New Paradigms for Control
Inverter-based resources (such as wind and solar) introduce major paradigm shift in power system control
  Decreasing impact of large synchronous machines with their stabilizing inertia
  Resources are less dispatchable
Changes at the “edge” of the grid
  Data centers for AI (huge load increase)
  Electric vehicles
  More controllable or price-sensitive demand resources
What do all of these have in common? Need for high-quality electric grid modeling and simulation to prepare for a resilient and sustainable future.

## Slide 20: The Smart Grid
The term “Smart Grid” dates officially to the 2007 “Energy Independence and Security Act”, Title 13 (“Smart Grid”)
  Use of digital information and control techniques
  Dynamic grid optimization with cyber-security
  Deployment of distributed resources including
  Customer participation and smart appliances
  Integration of storage including PHEVs
  Development of interoperability standards

## Slide 21: NERC Reliability Coordinators
https://www.nerc.com/pa/rrm/TLR/Pages/Reliability-Coordinators.aspx
NERC is the North American Electric Reliability Corporation

## Slide 22: Transmission Lines and the Elements
Ike in Beaumont
Quebec Ice Storm

## Slide 23: Transmission Lines and Trees
We like trees, and they grow; but when trees get close to lines bad things can occur.
Before “Trimming”
After “Trimming”

## Slide 24: 230/115 kV Transformer Picture

## Slide 25: Residential Distribution Transformers
Residential single phase electric service uses a center tapped transformer to provide 240/120 volt service; a separate ground is used for safety

## Slide 26: Power System Time Frames
Image source: P.W. Sauer, M.A. Pai, Power System Dynamics and Stability, 1997, Fig 1.2, modified

## Slide 27: Important Electric Grid Considerations
Electricity cannot be economically stored
  Generation must be continually adjusted to match changes in electric load and losses
Electric power flows on high voltage transmission lines cannot usually be directly controlled
  Control is mostly indirect, by changing generation
Customers have been in control of their load
Transmission system has finite limits; often operated close to its limit for economic reasons

## Slide 28: Power System Components
Major Components:
  Generators
    Power conversion technology, regulation and control
  Transmission System (69 kV and above)
    Substations, transmission lines, power transformers, control devices
  Distribution System (below 69 kV)
    Distribution feeders, service transformers, metering and control
  Loads
    Customer electricity demands, patterns, quality

## Slide 29: Voltage Levels Usage Table
These voltages are measured Line-to-Line (except single phase LV)
Recall, Line-to-Neutral is less by a factor of
Many voltages are in use in U.S. power systems—here are some of the main ones.
"High Voltage", "Low Voltage" are relative terms, sometimes all can be labeled "High Voltage"
The labels given are typical
Level | Typical Voltages | Usage
Low Voltage | 120 V, 208 V, 240 V, 600 V | Customer-level loads, residential, commercial, smaller industrial
Medium Voltage | 4.16 kV, 12.47 kV, 13.8 kV, 20 kV, 22 kV, 34.5 kV | Distribution feeders, generator step-up, larger industrial motors
High Voltage | 69 kV, 100 kV, 115 kV, 138 kV, 161 kV, 230 kV | Transmission system network
Extra High Voltage (EHV) | 345 kV, 500 kV, 765 kV | Backbone of large transmission systems

## Slide 30: Labs
The first two labs (and most of the others) will involve power system simulation on PowerWorld Simulator
This will be in the labs in Zach 326 – not pictured
TAs will introduce more lab policies on the first week, which is next week
The main objective of the first two labs is to get familiar with the software and learn some basics about power system operations on smaller and medium-sized grid models

## Slide 31: Computer Tools for Power System Analysis
Positive Sequence Transmission Simulation
  Siemens PSSE – Common in East
  GE PSLF – Common in West
  PowerWorld
  ETAP
  Matpower - free, mostly in academia
Distribution, Unbalanced
  OpenDSS – free, open source
  GridLabD
  CYME
Electromagnetic Transients
  EMTP-RV
  PSCAD
Custom code – your own or in-house
https://new.siemens.com/global/en/products/energy/energy-automation-and-smart-grid/pss-software/pss-e.html

## Slide 32: PowerWorld Simulator
Commercial tool in actual use by utilities and others (1000+ customers in 70 countries)
Originally developed in 1996 by Prof. Overbye (formerly at University of Illinois, now at Texas A&M)
Originally designed to be well-suited to teaching students about power systems. Still has that capability while being full-featured for industry use
Strengths are user-friendliness and advanced data visualization
There is a free student 42-bus version. We will use full (unlimited bus) version for labs in this class.
powerworld.com

## Slide 33: Lab 1 – Part A
Objectives:
  Learn the basics of using PowerWorld Simulator to model balanced three-phase systems.
  Correct the power factor of three-phase load by proper placement of shunt capacitors.
  Learn the basics of power system operations in the quasi-steady-state (power flow) time frame
Tasks
  Explore impact of capacitor on different system metrics: losses, voltage.
  Add two additional lines to connect bus 3.

## Slide 34: Lab 1 – Part B
Tasks
  Run system and observe how load increases and flows and generation respond in a two-area system
Manually adjust generation during load increase
Attempt to manage area control error (ACE)
Observe the operation of automated ACE control by the generators

## Slide 35: Lab 1 – Last Step
Extreme loading of 42 bus system

## Slide 36: Lab 2 – Aggieland Power and Light
Fix problems on this grid using various control options
  Generator setpoints
  Phase shifting transformer
  Capacitor bank switching
  Transformer tap switching
Use a sensitivity-based approach to estimate impacts of control variables

## Slide 37: Synthetic Texas Grid
This 2000 bus grid will be used a lot in class and lab this semester
It is similar in some ways to the actual Texas grid: similar generation, load patterns, same geography. However, it is a fictitious (synthetic) transmission network: different voltages, all fictional lines and substations.
Data on actual Texas grid is too confidential to be used in class
This grid model was developed by researchers here in the Texas A&M Power and Energy research group and is being used in a lot of research projects.